## Slide 1
Machine Vision Pipeline for Steel Surface Defects Detection using FPGA SoC
STUDENT
Aaliyan Mansoor CS-21146 (3.1)
Muhammad Babar Ali CS-21145 (2.9)
Mohib Ud Din CS-21142 (2.7)
Muhammad Maaz Khan CS-21019 (2.6)
SUPERVISOR
Ms. Fakhra Aftab
Tuesday, 17/12/24
Computer & Information Systems Engineering , NED University of Engineering and Technology
CO-SUPERVISOR
Dr. Majida Kazmi

## Slide 2
Table of Contents
Introduction & Background
Task Division
Literature Review
Conclusion & Future Plan
I
II
III
IV
VI
3
6
7
9
11
Page
Milestones Achieved Summary
V
Data Preprocessing
Model Training & Optimization
FPGA Deployment
VII
VIII
13
17
19

## Slide 3
Introduction and Background
I
  Steel Surface Defects: Critical for industries (automotive, aerospace, manufacturing).
  Types of Defects: Cracks, inclusions, scratches, pitted surfaces.
  Challenges:
  Traditional methods: slow, manual, low precision.
  GPUs/CPUs: High energy usage, slower processing.
  Solution: FPGA-based Machine Vision Pipeline
  High accuracy, energy efficiency
3
Introduction
Significance and Motivation
  Combines Deep Learning with FPGA Efficiency.
  Solves trade-offs:
  Speed, Accuracy, Energy Efficiency.
  Aligns with Smart Manufacturing goals:
  Automation, energy efficiency, and quality assurance.
  Sets a benchmark for AI solutions in resource-constrained environments.

## Slide 4
Introduction and Background
I
Aim: Steel surface defect detection using FPGA SoC.
Objectives:
  Develop a robust deep learning model for defect detection.
  Preprocess and optimize datasets.
  Deploy the model on FPGA for high-speed, low-power inference.
  Evaluate metrics:
    Accuracy, Latency, and Energy Efficiency.
  Benchmark against CPU and GPU-based systems.
  Ensure scalability for industrial adoption.
4
Aims and Objectives
Methodology
  Dataset Preparation
  Model Selection and Training
  FPGA Deployment
  Performance Evaluation
  Comparative Analysis

## Slide 5
Introduction and Background
I
Visual Flowchart:
Machine Vision Pipeline for Steel Surface Defect Detection.
5
Machine Vision Pipeline

## Slide 6
Task Division
I
Task Division
6
  Aaliyan Mansoor: Performed model inspection and quantization, data preprocessing (AgriAutos dataset)
  Muhammad Babar Ali: Performed model inspection and quantization, model training and optimization
  Mohib Ud Din: Performed data preprocessing (NEUDET+GC10DET), model training and optimization
  Muhammad Maaz Khan: Performed data preprocessing (NEUDET), model inspection and quantization
Literature review and report writing was done collectively by all members.

## Slide 7
Milestones Achieved Summary
I
  Dataset Preparation
7
  Datasets Used:
  NEU-DET, GC10-DET (Public Datasets)
  Agriauto Industry-Specific Dataset
  Key Tasks:
  Data inspection, annotation, augmentation (Roboflow).
2.Model Selection and Training
  Compared YOLOv3 and YOLOv5 for speed, accuracy, and resource utilization.
  Selected Model: YOLOv5n (lightweight, fast, accurate).
  Optimization: Hyperparameter tuning, iterative training.
3.Model Deployment on FPGA
  FPGA Board: Avnet Ultra96-V2 (Zynq UltraScale+ MPSoC).
  Vitis AI Workflow:
  Model Inspection, Quantization (INT8).
  Initial Deployment of YOLOv5n.

## Slide 8
Milestones Achieved Summary (Gantt Chart)
I
Gantt Chart
8

## Slide 9
Literature Review
II
9
Literature Review
  Purpose: To review advancements in machine vision for steel surface defect detection and deployment on FPGA SoC.
  Resources Used: IEEE, ElsvierScopus & SpringerLink
  Key Insights:
    YOLO models most widely used for deployment on FPGAs
    Publicly available datasets widely used for comparison of models
    Performance metrics used to evaluate models
    Advantages of FPGAs over CPUs and GPUs
    Challanges faced in model deployment on FPGAs
  Impact on Project: shaped project objectives, provided a guided methodology and focus toward innovation

## Slide 10
Literature Review (Table)
II
10

## Slide 11
Data Preprocessing
II
11
Key Steps in Data Preprocessing
1.Data Inspection
  Filtered clear, noise-free images.
  Discarded low-resolution and blurry images.
2.Data Annotation
  Annotated using Roboflow with bounding boxes:
    Categories: Cracks, Inclusions, Scratches
  Exported in YOLOv5-compatible format.
3.Data Augmentation
  Techniques Applied:
    90° Rotations: Clockwise, Counterclockwise, Upside-down.
    Crop: Up to 10% zoom.
    Rotation: Random angles (-10° to +10°).
    Cutout: Simulated occlusions.
  Outcome: 3 augmented versions per image for dataset diversity.

## Slide 12
Data Preprocessing
II
12
Key Steps in Data Preprocessing
5.Conversion and Organization
  Annotation Format: [class_id, x_center, y_center, width, height]
  Directory Structure:
    images: Train, Val, Test
    labels: Corresponding .txt annotations
4.Dataset Split
  Train: 80%
  Validation: 10%
  Test: 10%
NEU-DET dataset defects
Defects on steel rods from Agriauto dataset

## Slide 13
Model Training & Optimization
III
13
Model Training & Optimization
  Model Options Available:
    comparing YOLOv3, YOLOv5, YOLOv7 and YOLOv11
    YOLOv7 and YOLOv11 excluded due to hardware constraints
  Comparing YOLOv3 and YOLOv5:
    YOLOv3 is faster than YOLOv5
    Although, YOLOv5 offers better accuracy
    However, YOLOv5 incorporates efficient network architecture thus requiring lesser memory bandwidth
  Comparing Variants of YOLOv5:
    YOLOv5x, YOLOv5l, and YOLOv5m require a lot of memory bandwidth
    YOLOv5n is the most widely used, FPGA friendly model offering a great balance between accuracy and performance

## Slide 14
Model Training & Optimization (Architecture)
IV
14
  Backbone: extract features from input image
  Neck: gathers information from various scales to find out defects of diversified sizes.
  Head: outputs bounding boxes and class probabilities for all
  Activation Functions: ReLU, LeakyReLU, Mish, SiLU

## Slide 15
Model Training & Optimization (Results)
IV
15
Training Parameters for YOLOv5n
Performance Metrics of YOLOv5n

## Slide 16
Model Training & Optimization (Results)
IV
16
Inference Results of YOLOv5n on NEU-DET+GC10-DET Dataset
Inference Results of YOLOv5n on Agriautos Dataset

## Slide 17
FPGA Deployment
IV
17
FPGA Deployment
  FPGA Board Used:
    Avnet Ultra96-v2, an ARM-based zynq Ultrascale+ MPSoC
    CLBs, LUTs
  Deployment Framework:
    Vitis-AI, developed by Xilinx to accelerate AI inference
    Deployment workflow:
      Environment Setup
      Quantization of float model
      Compiling quantized model
      Deployment on FPGA board

## Slide 18
FPGA Deployment (Inspection & Quantization)
IV
18
Inspection & Quantization
  Inspection: check if model is quantizable in it’s current form
  Preparation:
    Yolov5 default activation function changed
    Permute and View functions in last layer of detection head removed
  Quantization:
    Conversion of weights and activations from Float32 to Int8
    To reduce computational complexity
    PTQ (Post Training Quantization) and QAT (Quantization Aware Training)

## Slide 19
Conclusion & Future Plans
V
Complete Deployment on FPGA
Using Vitis-AI and deployment software, complete implementation of the model on the FPGA hardware.
Evaluate the deployed system for accuracy, FPS ,and resource utilization. Optimize and improve the system to achieve the best possible results.
Interface Development
Design a user-friendly interface for system operation and defect analysis.
19
Extensive Testing & Optimization of Deployed Model

## Slide 20
Thank you!
The End